## Slide 1
BIOGLOW · ROBOT DESIGN
Six teams built six robots.
The good ones all made the same choices.
Before we build ours, let's look at what other people already worked out — and at the mistakes they only found after building.
None of this is guesswork. It comes from a coach with ten years of seasons behind him, through regionals and nationals to an international final.
The robot that wins is not the cleverest one. It is the one that does the same thing every single time.

## Slide 2
THE BIG IDEA
One base. Many attachments.
Do not build a robot per mission. Build one really good base that never changes, then build a small attachment for each job that clips onto it. The base is the thing you get reliable once; the attachments are where the cleverness goes.
FIXED
One base
Never changes
Attachment for one job
Attachment for another
And another
TIME IS THE THING YOU RUN OUT OF. A BASE THAT NEVER CHANGES IS A BASE YOU ONLY DEBUG ONCE.

## Slide 3
THE LINE-UP
What each one is good at, and what it costs
Read the right-hand column carefully. That is where the lesson is.
Robot | What it does well | What it costs you
HummerOne Pro | Easiest to build. One kit plus the expansion set. Simple clip-on attachments. | Wheels slip once an attachment gets heavy.
Xbot | Frame right around the outside, so it balances well. Attachments on top and front. | The frame eats a lot of LEGO. Wheels can still slip — blue SPIKE wheels.
YellowBot v1 | Box frame lines up against walls. Attachments drop in using gravity. Colour sensor at the front. | Wheels can still slip — blue SPIKE wheels.
YellowBot v2 | Better box frame. Front-wheel drive. Hub sunk down low. Side walls can push things. | Raised frame needs extra LEGO. Needs 62.4 mm wheels.
Track-X | Sits very low, so it grips. Very accurate and repeatable. Fast frame swaps. Widely used. | Needs 62.4 mm wheels. Open sides, so no walls to line up with.
Boxor | Newest. Low, accurate, fast to swap, and a box frame for lining up. Best attachment system. | Needs 62.4 mm wheels.
Boxor is not better because it is newer. It is better because it collected the good ideas from the five before it.

## Slide 4
SPOT THE PATTERN
Three robots slip. Three don't. Why?
Sort the six by which wheels they use. The slipping stops exactly where the wheels change — and a coach who made that swap on a real team says the accuracy improved dramatically, with the robot no longer slipping on turns.
BLUE SPIKE WHEELS
HummerOne Pro
Xbot
YellowBot v1
All three list slipping
62.4 MM WHEELS
YellowBot v2
Track-X
Boxor
None of them do
THE 62.4 MM WHEEL IS ALSO BIGGER, SO IT DRIVES FASTER. MORE GRIP AND MORE SPEED, SAME PART.

## Slide 5
DESIGN RULE 1
A box frame lines you up for free
Push a box flat against the wall and it can only sit one way — square. That is a free, perfect starting position, every single run, with no code at all.
BORDER WALL
Open sides
Only one corner touches. It can sit
crooked and you will not notice.
HUB
Box frame
The whole edge touches, so it is square
before it moves. Same start, every run.
TRACK-X IS FAST AND ACCURATE BUT HAS OPEN SIDES. BOXOR KEPT THE SPEED AND ADDED THE FRAME.

## Slide 6
DESIGN RULE 2
Keep the weight low — and even
Weight up high makes the robot rock when it starts, stops and turns. Rocking lifts weight off the wheels, and a wheel with no weight on it spins instead of driving. Weight also needs spreading front to back: pile it all at one end and your turns stop being repeatable.
MAT
HUB
Hub on top
Weight sits high. It rocks.
Hub sunk into the frame
Weight stays on the wheels.
DOT = WHERE THE WEIGHT AVERAGES OUT. LOWER IS BETTER, AND CENTRED IS BETTER STILL.

## Slide 7
DESIGN RULE 3
Hold the wheels straight
Support the wheel on the motor side and on the far side. A heavy attachment — say you are carrying something across the table — presses down and bends the wheels slightly inward. You will not see it happen. You will only see the robot stop driving straight.
Braced one side
DRIFTS
The axle flexes, the wheel leans, and every
run ends somewhere slightly different.
Braced both sides
STRAIGHT
The wheel stays square, so the same
program gives the same result.
TOP VIEW · GREY = FRAME BEAM

## Slide 8
DESIGN RULE 4
Attachments should drop on, not screw on
In a match you get two and a half minutes. Every second spent wrestling an attachment is a second not scoring. This is the gravity technique: a couple of small pegs guide it into place, then its own weight holds it. Nothing locks.
Attachment
DROPS IN
Chassis
TOP MOUNT
FRONT MOUNT
Held by its own weight
No pins to line up
under pressure.

## Slide 9
DESIGN RULE 5
The gyro does the driving, not the motor blocks
The ready-made movement blocks look easy and they will let you down. Zero the gyro at the start, then hold that heading the whole way, correcting continuously. Bump a model mid-run and it steers itself back to zero.
Zero the gyro, then hold the heading.
Drive at 0°, measure the error constantly, steer by an amount proportional to how far off you are.
Motor encoders for distance.
Exact degrees forward, exact degrees to turn. Repeatable in a way that timing never is.
One colour sensor is still worth having.
But black lines are disappearing from FIRST's mats, so most teams now navigate on gyro and encoders.
Four wheels with rubber tyres.
Not a ball-bearing castor. Four driven wheels track straighter.
We already have this: the Acceleration block ramps up, holds the gyro heading and eases off — and the same maths is drive_cm_gyro in the Python toolkit.

## Slide 10
OUR TURN
What we are deciding this week
We do not have to invent a robot. We have to make these choices on purpose, and be able to say why — because that is the question the judges ask.
Is the base finished, and can we leave it alone?
Box frame or open sides?
Which wheels?
Where does the hub sit, and is the weight even?
Are the wheels supported on both sides?
How fast can we swap an attachment?
Top mount, front mount, or both?
Gyro and encoders, or the ready-made blocks?
Write down what we choose and why, and photograph version one before we take it apart — that record is what the judges score hardest.